## Slide 1: Data
Spring 2019/2020
wilkie
(with content borrowed from Vinicius Petrucci and Jarrett Billingsley)
CS/COE 0449 Introduction to Systems Software
Representation
2

## Slide 2: Binary Encoding
Bits, Bytes, and Nybbles

## Slide 3: Positional Number Systems
The numbers we use are written positionally: the position of a digit within the number has a meaning.
1,234
1s
10s
100s
1000s
100
101
102
103
1 × 103 +
2 × 102 +
3 × 101 +
4 × 100
=
Most Significant
Least Significant
How many digit symbols do we have in our number system?
  10: 0, 1, 2, 3, 4, 5 ,6 ,7, 8, 9

## Slide 4: Ranges of Representation
Suppose we have a 4-digit numeric display.
What is the smallest number it can show?
What is the biggest number it can show?
How many different numbers can it show?
  9999 - 0 + 1 = 10,000
What power of 10 is 10,000?
  104
With n digits:
  We can represent 10n numbers
  The largest number is 10n-1

## Slide 5: Numeric Bases
These 10s keep popping up… and for good reason
We use a base-10 (decimal) numbering system
  10 different digits, and each place is a power of 10
But we can use (almost) any number as a base!
The most common bases when dealing with computers are base-2 (binary) and base-16 (hexadecimal)
When dealing with multiple bases, you can write the base as a subscript to be explicit about it:
510 = 1012

## Slide 6: Let’s make a base-2 system
Given base B,
  There are B digit symbols
  Each place is worth Bi, starting with i = 0 on the right
  Given n digits,
    You can represent Bn numbers
    The largest representable number is Bn – 1
So how about base-2?

## Slide 7: Binary (base-2)
We call a Binary digIT a bit – a single 1 or 0
When we say an n-bit number, we mean one with n binary digits
27 26 25 24 23 22 21 20
1001 0110
128s 64s 32s 16s 8s 4s 2s 1s
1 × 128 +
0 × 64 +
0 × 32 +
1 × 16 +
0 × 8 +
1 × 4 +
1 × 2 +
0 × 1
= 15010
=
To convert binary to decimal: ignore 0s, add up place values wherever you see a 1.
MSB LSB

## Slide 8: Bits, Bytes, Nybbles, and Words
A bit is one binary digit, and its unit is lowercase b.
A byte is an 8-bit value, and its unit is UPPERCASE B.
  This is why your 30 megabit (Mb/s) internet connection can only give you at most 3.75 megabytes (MB) per second!
A nybble (awww!) is 4 bits – half of a byte.
  Corresponds nicely to a single hex digit.
A word is the "most comfortable size" of number for a CPU.
When we say "32-bit CPU," we mean its word size is 32 bits.
  This means it can, for example, add two 32-bit numbers at once.
BUT WATCH OUT:
  Some things (Windows, x86) use word to mean 16 bits and double word (or dword) to mean 32 bits.

## Slide 9: Why binary? Whynary?
Because it's the easiest thing to implement!
Basic arithmetic is a bit easier.
So, everything on a computer is represented in binary.
  everything.
  EVERYTHING.
  01000101 01010110 01000101 01010010 01011001 01010100 01001000 01001001 01001110 01000111 00101110
    (“EVERYTHING.”)

## Slide 10: Binary Representation
Computers translate electrical signals to either 0 or 1.
It is relatively easy to devise electronics that operate this way.
In reality, there is no such thing as “binary” so we often have to approximate and mitigate error.
Oscilloscope visualization of several digital wires. From @computerfact on Twitter.

## Slide 11: Integer Encoding
Casting is Not Just a Witch or Wizard Thing

## Slide 12: Hexadecimal
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary
Binary numbers can get really long, quickly.
  3,927,66410 = 11 1011 1110 1110 0111 00002
But nice "round" numbers in binary look arbitrary in decimal.
  10000000000000002 = 32,76810
This is because 10 is not a power of 2!
We could use base-4, base-8, base-16, base-32, etc.
  Base-4 is not much terser than binary
    e.g. 3,927,66410 = 120 3331 2323 00004
  Base-32 would require 32 digit symbols. Yeesh.
    They do, oddly, have their place… but not really in this context.
  Base-8 and base-16 look promising!

## Slide 13: Hexadecimal or “hex” (base-16)
Digit symbols after 9 are A-F, meaning 10-15 respectively.
Usually we call one hexadecimal digit a hex digit. No fancy name :(
167 166 165 164 163 162 161 160
003B EE70
0 × 167 +
0 × 166 +
3 × 165 +
11 × 164 +
14 × 163 +
14 × 162 +
7 × 161 +
0 × 160 =
3,927,66410
=
To convert hex to decimal: use a dang calculator lol

## Slide 14: Binary to Hex (animated)
1100
1010
0010
0000
0010
0001
0110
0100
4
C
A
2
0
2
6
1
0x4CA20261
32-bits! (Not so bad…)
Q: Create a random binary string and practice!

## Slide 15: Signed Numbers (sign-magnitude)
Seems like a good time to think about “negative” values.
  These are numbers that have nothing good to say.
Binary numbers have bits which are either 0 or 1.
  Well, yeah…
So what if we used one bit to designate “positive” or “negative”
  Called sign-magnitude encoding:
10100010 =
-34
00010110 =
22 (normal)

## Slide 16: Signed Numbers (problems)
Waaaaait a second.
  What is negative zero???
This encoding allows two different zeros.
  This means we can represent how many different values (8-bit)?
    28 – 1 (minus the one redundant value) = 255 (-127 … 0 … 127)
Sign-magnitude is a little naïve… let’s try a different approach…
10000000 =
-0
00000000 =
0

## Slide 17: Signed Numbers (2’s Complement)
This one, I promise, is juuuuust right.
  But it’s a little strange!
We’ll just make SURE there is only one zero:
So, we flip the bits… and add one.
  Adding one makes sure our -0 is used for -1 instead!
Sure, it’s a little lopsided, but, hey, we get an extra number.
  But, hmm, but -4 doesn’t have a valid positive number.
    That’s the trade-off, but it’s for the best.
110
-2
101
-3
0
000
001
+1
010
+2
011
+3
111
-1
100
-4
0
000
001
+1
010
+2
011
+3
101
-1
110
-2
111
-3
100
Signed Magnitude
2’s Complement
😘

## Slide 18: Signed Numbers (2’s Complement)
Let’s look some examples:
If the MSB is 1: Flip! Add one!
Otherwise: Do nothing! It’s the same!
11010100=
-00101011=-(43+1)=-44
00000000=
00000000= 0
11111111=
-00000000=-(0+1) =-1
00100110=
00100110= 38

## Slide 19: Signed Numbers (2’s Complement)
What happens when we add zeros to a positive number:
What happens when we add ones to a negative number:
00100110 = 38
0000000000100110 = ?
10100110 = ?
11111111110100110 =
-00000000001011001 = ?
-90
38
-90
Dang that’s cool!
10100110 = ?
-(01011001+1) = ?
-01011010 = ?
-90

## Slide 20: Can I Get an Extension?
Sometimes you need to widen a number with fewer bits to more
zero extension is easy: put 0s at the beginning.
10012  to 8 bits  0000 10012
But there are also signed numbers… what about those?
  The top bit (MSB) of signed numbers determines the sign (+/-)
sign extension puts copies of the sign bit at the beginning
10012  to 8 bits  1111 10012
00102  to 8 bits  0000 00102
Q: What happens when you sign extend the largest unsigned value?

## Slide 21: Absolutely Bonkers
public class AbsTest {
public static int abs(int x) {
if (x < 0) {
x = -x;
}
return x;
}
public static void main(String[] args) {
System.out.println(
String.format("|%d| = %d", Integer.MIN_VALUE, AbsTest.abs(Integer.MIN_VALUE))
);
}
} // Outputs: |-2147483648| = -2147483648
Q: How many bits is a Java int? What happened here?

## Slide 22: Integer Ranges
Recall:
  The range of an unsigned integer is 0 to 2n – 1
  Q: Why do we subtract 1?
What is the range of a 2’s complement number?
  Consider the sign bit, how many negative integers?
  Consider, now, the positive integers.
  Remember 0.
-2n-1 to 2n-1 – 1
Q: What if you needed a range with far more negatives than positives?

## Slide 23: Integers in C
C allows for variables to be declared as either signed or unsigned.
  Remember: “signed” does not mean “negative” just that it can be negative.
An unsigned integer variable has a range from 0 to 2n – 1
And signed integers are usually 2’s complement: 2n-1 to 2n-1 – 1
  Where “n” is determined by the variable’s size in bits.
Integer Types: (signed by default, their sizes are arbitrary!!)
  char unsigned char 8 bits (byte)
  short int unsigned short int 16 bits (half-word)
  int unsigned int 32 bits (word)
  long int unsigned long int 64 bits (double-word)
Usually no strong reason to use anything other than (un)signed int.
Q: What is the range of a signed char?

## Slide 24: Integers in C: Limits
Since sizes of integers are technically arbitrary…
  They are usually based on the underlying architecture.
… C provides standard library constants defining the ranges.
  https://pubs.opengroup.org/onlinepubs/009695399/basedefs/limits.h.html
#include <limits.h> // Provides INT_MAX etc
#include <stdio.h> // Provides printf
int main() {
printf("%d ", INT_MAX); // Print the maximum signed int
printf("%u\n", UINT_MAX); // Print the maximum unsigned int
return 0;
} // Output: 2147483647 4294967295
Q: Experiment with using "%d" for both. What is the result?

## Slide 25: Casting
C lets you move a value from an unsigned integer variable to a signed integer variable. (and vice versa)
However, this is not always valid! Yet, it will do it anyway.
  The binary value is the same, its interpretation is not!
    This is called coercion, and this is a relatively simple case of it.
  Since it ignores obvious invalid operations this is sometimes referred to as “weak” typing.
  The strong/weak terminology has had very fragile definitions over the years and are arguably useless in our context. Let’s ignore them.
Moving values between different types is called casting
  Which sounds magical and it sometimes is.
Q: What is true of the result of casting the value -1 to an unsigned type?